| Operational Area | Roles and Responsibilities | MATOC/RITIS | CapWIN | DDOT | Local Roadway Agencies | Maryland State Highway Administration (MDSHA) | MWCOG | National Park Service | Public Safety and Emergency Management (VA MD DC) | Regional ISP | Regional Local Transit Operators | Regional Toll Operations (Smart-Tag Center/Greenway/MdTA) | Regional Transit Clearance House | VDOT NOVA District /VDOT | VRE Center | WMATA | None (not undertaken as a regional activity) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Surface Street Management | Manage drawbridges at rivers and canals and other multimodal crossings. This includes control devices (e.g., gates, warning lights, dynamic message signs) at the drawbridge as well as the information systems that are used to keep travelers appraised of current and forecasted drawbridge status. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides for the management of reversible lane facilities, which includes sensory functions that detect wrong-way vehicles and other special surveillance capabilities that mitigate safety hazards associated with reversible lanes. |  |  | X | A? | X |  |  |  |  |  |  |  |  |  |  |  | Montgomery Co. has reversible lanes, others may. Do these agencies have the "special capabilities" mentioned? |
|  | Monitors traffic conditions using fixed equipment such as loop detectors and CCTV cameras. |  |  | A? | A? | A? |  |  |  | A? |  |  |  | A? |  |  |  | If traffic monitoring is to be considered a regional (multi-jurisdictional) activity, then these should be added. We now have private sector (ISP) – installed monitoring devices that are shared across agencies. |
|  | Provide the interface between roadway devices and other roadway devices (considered to be contained in the Other Roadway terminator) for the exchange of data, status, and control. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides monitoring and remote diagnostics of field equipment to detect field equipment failures, issues problem reports, and tracks the repair or replacement of the failed equipment. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Manages highway traffic at highway-rail intersections (HRIs) where operational requirements do not dictate advanced features (e.g., where rail operational speeds are less than 80 miles per hour). |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Coordinates field equipment that is distributed along the roadway by supporting direct communications between field equipment. This includes coordination between remote sensors and field devices (e.g., Dynamic Message Signs) and coordination between the field devices themselves (e.g., coordination between traffic controllers that are controlling adjacent intersections.). |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Assist in coordinating traffic signals across boundaries. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Closes roadways to vehicular traffic when driving conditions are unsafe, maintenance must be performed, and other scenarios where access to the roadway must be prohibited. |  |  | A? | A? | A? |  | A? | A? |  |  |  |  | A? |  |  |  | Are road closures by definition a regional (interjurisdictional) activity? |
|  | Monitors the speeds of vehicles traveling through a roadway system. If the speed is determine to be excessive, roadside equipment can suggest a safe driving speed. Also support notifications to an enforcement agency to enforce the speed limit on a roadway system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides an alternative approach for surveillance of the roadway network. Two general implementation paths are supported by this method: 1) wide-area wireless communications between the vehicle and Information Service Provider is used to communicate current vehicle location and status, and 2) dedicated short range communications between the vehicle and roadside is used to provide equivalent information directly to the Traffic Management Center. |  |  |  |  | A? |  |  |  |  |  |  |  |  |  |  |  | MMTIS |
|  | Provide Surveillance and Control, and maintenance of signal system. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Monitors individual vehicle emissions and provides general air quality monitoring using distributed sensors to collect the data. Both area wide air quality monitoring and point emissions monitoring are supported by this function. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides advanced algorithms, processing, and mass storage capabilities that support historical evaluation, real-time assessment, and forecast of the roadway network performance. This includes the prediction of travel demand patterns to support better link travel time forecasts. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Provides for the sharing of traffic information and control among traffic management centers to support a regional control strategy. | A? |  | A? |  | A? |  |  |  |  |  |  |  | A? |  | A? |  | Consider editing the words "regional CONTROL strategy" |
|  | Monitors highway-rail intersection (HRI) equipment at the roadside which manages highway traffic. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Report and Coordinate road closures with other transportation agencies. | X |  | X | X | X |  | X |  |  |  |  |  | X |  | A? |  | Is WMATA sometimes a source of this information to other agencies (e.g. local transit)? |
|  | Maintain and operate the backup TMC, as necessary. |  |  | X | X | X |  |  |  |  |  |  |  | A? |  | A? |  |  |
|  | Provide communications with other systems, such as CHART, CapWIN, RITIS, etc. | X |  | X | X | X |  |  |  | A? |  |  |  | X |  | A? |  | WMATA and ISPs may share information with other systems. |
|  | Coordinate traffic signal response at highway-rail intersections. |  |  |  | X | X |  |  |  |  |  |  |  | X |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Maintain centralized signal system. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Install appropriate detection and dissemination devices along major corridors. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  | May need to clarify. |
|  | Implement traffic control response to emergencies/incidents. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Manage regional signal timing coordination program. | X |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Maintain field equipment. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Monitor and manage traffic on designated arterials and freeways. | X |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Receive signal priority requests from transit operators (where applicable). |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Provide transit signal priority response (where applicable). |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Receive preemption requests from emergency vehicle operators (where applicable). |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Provide preemption response (where appropriate). |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Assist in coordinating traffic signals across boundaries. | A? |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  | Will MATOC assist with traffic signals? |
|  | Share traffic information with other transportation agencies. | X |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Monitor weather conditions along roadways. |  |  | A? | X | X |  |  |  |  |  |  |  | X |  |  |  | Does DDOT monitor weather? |
|  | Coordinate traffic control response to incidents with other transportation agencies. | X |  | X | X | X |  | X |  |  |  |  |  | X |  |  |  |  |
| Freeway Management | Utilize surveillance information for detection of incidents. | A? | A? | A? | A? | A? |  |  |  |  |  |  |  | A? |  | A? |  | MATOC-related function? |
|  | Manages HOV lanes by coordinating freeway ramp meters and connector signals with HOV lane usage signals. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides the communications and roadside equipment to support ramp control, lane controls, and interchange control for freeways. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Monitor weather conditions along freeways | X |  |  | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Manage and monitor traffic on freeway on-ramps and highways. |  |  | X |  | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Manage and monitor traffic on freeways including HOV lane management. |  |  |  | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Provides the capability to detect the HOV lane usage using sensor equipment. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Share traffic information with other transportation agencies. | X |  | X | X | X |  |  |  |  |  |  |  | X |  | A? |  | Will WMATA be called upon to share information it has received with other transit agencies (e.g., RESF-1 Level A/Level B)? |
|  | Provides the roadside elements of traffic information dissemination including DMS, HAR, and talking pedestrian signs. |  |  | X | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Collect and process automated traffic data from traffic speed monitoring sites. |  |  |  | X | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Monitor pavement conditions during inclement weather. |  |  |  |  | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Utilize current technology and strategies to optimize flow of traffic on access controlled highways. |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Employ strategies to improve the efficiency of operations at inter-modal transfer points. |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |
| Incident Management | Propose and facilitate the appropriate dissemination of incident related information to travelers and potential travelers. | X | X | X |  | X |  |  |  |  | A? |  |  | X |  | A? |  | Transit agencies provide traveler information. |
|  | Implement algorithms for automated detection of incidents using data from roadways sensors and provide verification. |  |  | X |  | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Track incidents and responses. | A? | X | X | A? | X |  |  | A? |  | A? |  |  | X |  | A? |  | MATOC-related function? |
|  | Provide resources when requested by emergency/incident management responders. |  |  | X | X | X |  |  | A? |  | A? |  |  | X |  | A? |  | There may be transit and public safety resources utilized. |
|  | Propose and facilitate the appropriate control of traffic signals and other traffic control to reduce the traffic flow impact of an incident. | A? | D? | X | X | X |  |  |  |  |  |  |  | X |  |  |  | MATOC function? Delete as a CapWIN function? |
|  | Provide the status of all resources needed for incident resolution to those agencies responding to the incident. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provide the capability to disseminate information relating to response status to other agencies. | A? | A? | A? | A? | A? |  |  | A? |  | A? |  |  | A? |  | A? |  | Need to discuss. |
|  | Allow coordinated selection/determination of the procedures, including alternate routes, needed for resolution of each incident and provide the procedures to those agencies responding to the incident. | A? | A? | A? | A? | A? |  |  | A? |  | A? |  |  | A? |  | A? |  | Need to discuss. |
|  | Interface with other transportation agencies to support coordinated emergency/incident response involving multiple agencies. | X | X | X | X | X |  |  | A? |  | A? |  |  | X |  | A? |  | Additional agencies undertake this activity. |
|  | Propose and facilitate the appropriate dispatch of service vehicles to an incident. |  |  | X | X | X |  |  | A? |  | A? |  |  | X |  | A? |  | Add transit and public safety? |
|  | Share appropriate detection and dissemination devices along major arterials with other transportation agencies. |  | X |  |  | X |  |  |  |  |  |  |  | X |  |  |  |  |
|  | Predict Hazardous Conditions, including the time and location of hazardous conditions that may cause an incident. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Provide the incident manager at the emergency/incident scene. |  |  | X | X | X |  | X | A? |  | A? |  |  | X |  | A? |  | Add transit and public safety? |
|  | Determine the expected traffic flow impact of each predicted incident. | A? |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | MATOC function? |
|  | Provides the capability to identify existing (both planned and unplanned) incidents. | A? | A? | A? | A? | A? |  |  | A? |  | A? |  |  | A? |  | A? |  | MATOC – related function? |
|  | Formulate appropriate response actions to each identified incident and revise those actions when necessary. | A? | A? | A? | A? | A? |  |  | A? |  | A? |  |  | A? |  | A? |  | MATOC – related function? |
| Electronic Toll Collection | Provides the capability to identify those vehicles and/or operators that violate its toll collection process. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Maintain and operate field and office toll collection facilities/equipment. |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |
|  | Manage toll collection process. |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |
|  | Provide the capability to automatically access and process each commercial vehicle's required documentation. |  |  |  |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |
|  | Assign appropriate toll credit to appropriate agencies. |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |
| Parking Management | Supports communication and coordination between equipped parking facilities and also supports regional coordination between parking facilities and traffic and transit management systems. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Provide the interface to a local parking lot operator that controls the use of the lot. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Detect and classify vehicles entering and exiting the parking facility and measures parking facility occupancy to support parking operations and traveler information services. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Supports electronic payment of parking fees |  |  |  |  |  |  |  |  |  |  |  |  | X |  | X |  | Verify that VDOT does this. |
|  | Manages parking reservations, parking lot use and revenue collection for parking facilities. |  |  |  |  |  |  |  |  |  |  |  |  | X |  | X |  | Verify that VDOT does this. |
|  | Determine and distribute the dynamic status of individual parking lots. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
|  | Maintain and distribute static information about individual parking lots. This information includes hours of operation, rates, lot location, lot entrance locations, lot capacity (number of spaces), lot type (Open Lot, Covered Garage, Permit Parking, Contract Parking, Free Parking - include P+R lot, Paid Parking, other) and lot constraints (heights, type of vehicles, etc.). |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Be responsible for maintaining a store of parking lot data. This data is used in transactions requiring electronic payment of parking lot services, as well as for a traveler making a parking lot reservation. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region. |
| Transit Services | Collects the latest available information for a transit service and makes it available to transit customers and to Information Service Providers for further distribution. |  |  |  |  |  |  |  |  |  |  |  | X |  |  | X |  |  |
|  | Provides train movement and wayside device monitoring and control, including third rail power |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Provide automatic train control, wayside device monitoring and control. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Provide on-bus fare boxes, garage and central fare processing equipment for fare collection and passenger counts. |  |  |  |  |  |  |  |  |  | A? |  |  |  |  | X |  |  |
|  | Provides dispatch function, and tracking for bus operators. |  |  |  |  |  |  |  |  |  | A? |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Provides automatic passenger counts. |  |  |  |  |  |  |  |  |  | X |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Monitors train movement in yards, and on mainline. Provides information about consist, railcar and train revenue and non-revenue mileage, schedule adherence. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Provide SmartTrip-SMRT service that provides overall management and coordination for fare collection programs, and ridership statistics. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |
|  | Support, implement, and operate in the regional fare management program. | D? |  |  |  |  |  |  |  |  | A? |  | A? |  | X | X |  | Delete as a MATOC function? |
|  | Collect transit operational data and load it into a data store for use by the routes and schedules generation processes. |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  | Need to discuss. |
|  | Provides the capability for transit vehicles to request signal priority through short range communication directly with traffic control equipment at the roadside. |  |  |  |  |  |  |  |  |  | X |  |  |  | D? | X |  | Delete VRE? |
|  | Provides the capability to automate planning and scheduling, allowing paratransit and flexible-route transit services to develop, print and disseminate schedules, and automatically update customer service operator systems with the most current schedule. |  |  |  |  |  |  |  |  |  |  |  | X |  |  | X |  | Need to discuss. |
|  | Act as the interface for advanced payment of tolls and parking lot charges from the traveler. |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |
|  | Provide the interface through which transit routes (including transfer points and clusters), schedules, fares and incident information can be exchanged with other transit centers. |  |  |  |  |  |  |  |  |  |  |  | X |  |  | X |  |  |
|  | Provide means of communication with bus operators, rail operators, station managers, interlockers, depot personnel, dispatch personnel, public safety personnel, and maintenance personnel. |  |  |  |  |  |  |  |  |  | A? |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Performs vehicle routing and scheduling, as well as automatic operator assignment and system monitoring for fixed-route and flexible-route transit services |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Should this be considered a regional activity? |
|  | Provides automatic transit maintenance scheduling and monitoring. On-board condition sensors monitor system status and transmit critical status information to the Transit Management Center. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides remote transit vehicle disabling by the Transit Management Center and transit vehicle operator authentication. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not undertaken in this region |
|  | Provides for the physical security of transit passengers and transit vehicle operators. On-board equipment is deployed to perform surveillance and sensor monitoring in order to warn of potentially hazardous situations. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provides the capability to assign vehicle operators to routes in a fair manner while minimizing labor and overtime services, including operator preferences and qualifications, and automatically tracking and validating the number of work hours performed by each individual operator. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Remove as not regional (undertaken within individual agencies only) |
|  | Provides the capability to automate planning and scheduling, allowing paratransit and flexible-route transit services to develop, print and disseminate schedules, and automatically update customer service operator systems with the most current schedule. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | This is a repeat of an earlier entry. |
|  | Forwards paratransit and flexible-route dispatch requests to the operator and forwards acknowledgements to the center. It coordinates with, and assists the operator in managing multi-stop runs associated with demand responsive, flexibly routed transit services. |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X |  | Should this be considered a regional activity? |
|  | Provide faregates, farecard vending machines, in-station and central facility fare processing equipment for rail system revenue collection and passenger counts. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Send fleet status and location information to operations center. |  |  |  |  |  |  |  |  |  | X |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Provide bus and commuter transit rail service. |  |  |  |  |  |  |  |  |  | A? |  |  |  | X |  |  | Addition for MARC. Need to discuss what the VRE center is. |
|  | Provides capability to determine the need for transit priority on routes and at certain intersections and request transit vehicle priority at these locations. It also supports schedule coordination between transit properties and coordinates with other surface and air transportation modes. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Not undertaken in this region. |
|  | Provide fixed route bus operations. |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X |  |  |
|  | Coordinate schedules with other transportation agencies. | X |  |  |  |  |  |  |  |  | X |  |  |  | X | X |  |  |
|  | Track and manage fleets using AVL technology and two-way communications with the fleet. |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X |  |  |
|  | Supports the capability for two-way voice communication between the transit vehicle operator and a facility, two-way data communication between the transit vehicles and a facility, on-board safety sensor data to be transmitted from the transit vehicles to a facility, and data transmission from individual facilities to a central facility for processing/analysis if desired. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
| Traveler Information | Provide in-station electronic signs that display train arrival information, schedule delay, incident information and ADA required access information. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Should this be considered a regional activity? |
|  | Provides a free e-mail subscription service to provide notice of elevator service disruptions at the Metrorail stations of choice. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |
|  | Provides yellow pages and reservation services to the user. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Not undertaken in this region. |
|  | Provides distribution of traffic and travel advisory information to drivers through in-vehicle devices. It includes short range communications between roadside equipment and the vehicle and wireline connections to the Traffic Management Center for coordination and control. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Not undertaken in this region. |
|  | Provides the capability to provide specific directions to travelers by receiving origin and destination requests from travelers, generating route plans, returning the calculated plans to the users, and then potentially logging the route plans with Traffic Management Center. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | WMATA Ride Guide? |
|  | Provide traffic, emergency, and incident information to drivers and other transportation agencies. |  |  | X | X | X |  |  |  | X |  |  |  | X |  |  |  |  |
|  | Provides dynamic rideshare matches, including rider and driver information and reservations. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D? | X | Delete as WMATA. Not undertaken in this region as a dynamic activity. |
|  | Collects traffic conditions, advisories, general public transportation, toll and parking information, incident information, roadway maintenance and construction information, air quality and weather information, and broadly disseminates this information through existing infrastructures and low cost user equipment (e.g., FM subcarrier, cellular data broadcast). |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Not undertaken in this region. |
|  | Provides advanced route planning and guidance which is responsive to current conditions, and supports collection of near-real time information on intended routes for a proportion of the vehicles in the network. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | Not undertaken in this region. |
|  | Tracks customer complaints and resolution; lost and found. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Should this be considered a regional activity? |
|  | Provides trip planning via web interface for entire jurisdiction including all carriers. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Need to discuss. |
|  | Provides internet website with bus and rail system maps, rail station information, parking information, bus & rail schedules (also downloadable to PDAs) and fares, trip planning, e-alerts and advisories (also subscription to same), accessibility, elevator/escalator status, |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |
|  | Provides customer services including: trip planning, fare information, customer complaints, incident information. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |
|  | Allow the traveling public to make better informed travel decisions by providing en-rout media information on travel condition. |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |
|  | Allow the traveling public to make better informed travel decisions by providing information on travel conditions through media accessible from home, work or other major ravel origins. |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |
|  | Provide real time transit information to travelers via Website, pager (or PDA), kiosk, or station signs. |  |  |  |  |  |  |  |  |  | X |  |  |  |  | X |  |  |
|  | Services voice-based traveler requests for information that supports traveler telephone information systems like 511. |  |  |  |  |  |  |  |  |  |  |  |  | X |  | A? |  | Add WMATA? |
|  | Install appropriate detection and dissemination devices. |  |  | X | X | X |  |  |  | X |  |  |  | X |  |  |  |  |
|  | Provide road weather conditions to other transportation agencies. |  |  | X |  | X |  |  |  |  |  |  |  | X |  |  |  |  |
| Emergency Management | Supports evacuation of the general public from a disaster area and manages subsequent reentry to the disaster area. |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provide the highest public safety for passengers, airport workers and checked baggage. |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Dispatch SSP patrol vehicles |  | X |  |  |  |  |  | X |  |  |  |  | X |  |  |  |  |
|  | Provides emergency response plans or event plans. | X | X |  |  | X |  |  | X |  |  |  |  |  |  | X |  |  |
|  | Conduct offensive operations to mitigate a hazardous materials emergency. |  | D? |  |  |  |  |  | X |  |  |  |  |  |  |  |  | Delete CapWIN. |
|  | Performs receiving Mayday messages and security alarms, determines an appropriate response, and either uses internal resources or contacts a local agency to provide that response. |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |  |  |  |
|  | Monitors transportation infrastructure (e.g., bridges, tunnels and management centers) for potential threats using sensors and surveillance equipment and barrier and safeguard systems to preclude an incident, control access during and after an incident or mitigate impact of an incident. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provides the management of barrier systems for transportation facilities and infrastructure. Barrier systems include automatic or remotely controlled gates, barriers and other systems intended to preclude an attack or control access during and after an incident. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Enhances the ability of the surface transportation system to respond to and recover from disasters. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Identifies the key points of integration between transportation systems and the public safety, emergency management, and other allied organizations that form the overall disaster response. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Dispatch police, fire, and ambulance vehicles. Provides for recording of calls, monitoring and recording of video, incident reporting to federal, state and local agencies. |  | X? |  |  |  |  |  | X |  |  |  |  |  |  | X |  | Need to discuss re CapWIN. |
|  | Supports coordination of evacuation plans among the federal, state, and local transportation, emergency, and law enforcement agencies that may be involved in a large-scale evacuation. |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provide disaster-related traveler information to the general public, including evacuation and reentry information and other information concerning the operation of the transportation system during a disaster. | A? |  | A? | A? | A? |  |  | A? |  | A? |  |  | A? |  | A? |  | Need to discuss. |
|  | Provides emergency information to assist the public with evacuations when necessary. Information on mandatory and voluntary evacuation zones, evacuation times, and instructions are provided. Available evacuation routes and destinations and current and anticipated travel conditions along those routes are provided so evacuees are prepared and know their destination and preferred evacuation route. |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Broadcast wide area alerts and advisories for emergency situations such as severe weather events, civil emergencies, child abduction (AMBER alert system), military activities, and other situations that pose a threat to life and property where information must be immediately provided to the traveling public. |  | A? | A? | A? | A? |  |  | A? |  | A? |  |  | A? |  | A? |  | Need to discuss. |
|  | Supports coordination of emergency response plans, including general plans developed before a disaster as well as specific tactical plans with short time horizon that are developed as part of a disaster response. |  |  |  |  |  |  |  | A? |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Perform other “non-transportation related” public safety duties. |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
|  | Participate in the call box program. |  |  |  |  |  |  |  | X? |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Receive landline public safety calls and forward to appropriate dispatch center. |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
|  | Monitors and detects potential, looming, and actual disasters including natural disasters and man-made disasters. |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
|  | Coordinates evacuation plans among allied agencies and manages evacuation and reentry of a population in the vicinity of a disaster or other emergency that poses a risk to public safety |  | X? |  |  |  |  |  | X |  |  |  |  |  |  | X? |  | Need to discuss. |
|  | Provide security for public facilities owned by the local agency. |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
|  | Maintain centralized emergency management system. |  | X? |  |  |  |  |  | X |  |  |  |  |  |  | X |  |  |
|  | Use real-time traffic information received from other transportation agencies to aid the dispatcher in selecting the emergency vehicle(s) and routes that will provide a timely response. |  | X? |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
|  | Track and manage emergency vehicle fleets using AVL technology and two-way communications with the vehicle fleet |  | X |  |  |  |  |  | X |  |  |  |  |  |  | X |  |  |
|  | Create, store, and utilize emergency/incident response plans to facilitate coordinated response. | A? | X |  |  | X |  |  | X |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Interface with other transportation agencies to support coordinated emergency response involving multiple Agencies | X | X |  |  | X |  |  | X |  |  |  |  |  |  | X |  |  |
|  | Monitor video images and audio surveillance data collected in secure areas, including those frequented by travelers (transit stops, rest areas, park and ride lots, modal interchange facilities, on-board transit vehicles, etc.), and those typically away from travelers (tunnels, bridges, roadway infrastructure, etc.). |  |  |  |  |  |  |  | X |  |  |  |  |  |  | X |  |  |
| Maintenance and Construction | Directs activity in work zones, controlling traffic through portable dynamic message signs (DMS) and informing other groups of activity (e.g., ISP, traffic management, other maintenance and construction centers) for better coordination management. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Automatically treats a roadway section based on environmental or atmospheric conditions. Treatments include fog dispersion, anti-icing chemicals, etc. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Manages winter road maintenance, tracking and controlling snow plow operations, roadway treatment (e.g., salt spraying and other material applications) based on weather information. |  |  | X |  | X |  |  |  |  |  |  |  | X |  | X |  |  |
|  | Collects current road and weather conditions using data collected from environmental sensors deployed on and about the roadway (or guideway in the case of transit related rail systems). In addition to fixed sensor stations at the roadside, sensing of the roadway environment can also occur from sensor systems located on Maintenance and Construction Vehicles and on-board sensors provided by auto manufacturers. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Performs vehicle maintenance scheduling and manages both routine and corrective maintenance activities on vehicles and other maintenance and construction equipment. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Tracks the location of maintenance and construction vehicles and other equipment to ascertain the progress of their activities. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Detects vehicle intrusions in work zones and warns crew workers and drivers of imminent encroachment or other potential safety hazards. Crew movements are also monitored so that the crew can be warned of movement beyond the designated safe zone. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Provides overall management and support for routine maintenance on a roadway system or right-of-way. |  |  | X |  | X |  |  |  |  |  |  |  | X |  |  |  | Should this be considered a regional activity? |
|  | Disseminate maintenance and construction activity to centers that can utilize it as part of their operations, or to the Information Service Providers who can provide the information to travelers. |  |  | X | A? | A? |  |  |  |  |  |  |  | X |  | A? |  | Need to discuss. |
|  | Provides numerous services for scheduled and unscheduled maintenance and construction on a roadway system or right-of-way. Maintenance services would include landscape maintenance, hazard removal (roadway debris, dead animals), routine maintenance activities (roadway cleaning, grass cutting), and repair and maintenance of both ITS and non-ITS equipment on the roadway (e.g., signs, traffic controllers, traffic detectors, dynamic message signs, traffic signals, CCTV, etc.). |  |  | X |  | X |  |  |  |  |  |  |  | X |  |  |  | Should this be considered a regional activity? |
|  | Control traffic through portable dynamic message signs (DMS) and informing other groups of activity (e.g., ISP, traffic management, other maintenance and construction centers) for better coordination management. |  |  |  |  | X |  |  |  |  |  |  |  | X |  |  |  | Add others? |
|  | Supports coordinated response to incidents |  |  | X | A? | X |  |  |  |  | A? |  |  | X |  | A? |  | Add others? |
|  | Maintain AVL systems for maintenance vehicles. |  |  |  |  |  |  |  |  |  |  |  |  | X |  | X |  |  |
| Archive Data system | Collects and archives traffic, roadway, and environmental information for use in off-line planning, research, and analysis. | X | X | X | X | X | X |  |  | A? |  |  |  | X |  | X |  |  |
|  | Provides automatic passenger counts and archive the data for analysis and research. |  |  |  |  | X? |  |  |  |  | A? |  |  |  |  | X |  |  |
|  | Provide Enterprise Geographic Information System to manage archived data for hazmat, safety, assets, bus stops, routes. |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | Need to discuss. |
|  | Provide the interface that allows the regional members to share data and retrieve information | X | X |  |  |  | X |  |  |  |  |  |  |  |  | X |  |  |
|  | Selects and formats data residing in an ITS archive to facilitate local, state, and federal government data reporting requirements. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X? | Not undertaken as a regional activity. |
|  | Provides capabilities to access "in-place" data from geographically dispersed archives and coordinate information exchange with a local data warehouse. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provides the specialized publishing, directory services, and transaction management functions associated with coordinating remote archives. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |
|  | Provides functionality and interface definitions that allow collection of data from multiple agencies and data sources spanning across modal and jurisdictional boundaries. It performs the additional transformations and provides the additional meta data management features that are necessary so that all this data can be managed in a single repository with consistent formats. On-line analysis and data mining features that are also included in this operation in addition to the basic query and reporting user access features. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Need to discuss. |